## Slide 1
Hindusthan
College of Arts & Science
An Autonomous College- Affiliated to Bharathiar University
Approved by AICTE and Govt of Tamilnadu
Accredited by NAAC- An ISO Certified Institution
Class: III BSc COSTUME DESIGN &FASHION
SUBJECT:TEXTILE FINISHING TECHNOLOGY

## Slide 2
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Wrinkle free finishes are broadly used in the textile industry to impart wrinkle-resistance to cellulosic materials such as cotton fabric. The application of wrinkle resistance (permanent or durable press) finishes on the fabric improves their wrinkle resistance property.

## Slide 3
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
PROCESS SEQUENCE OF WRINKLE FREE FINISH:
Several process for wrinkle free/durable press items and fabrics are out lined here.
Pre cured process
Post cured process
The immersion process
Metered addition
Vapor – phase finish

## Slide 4
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Pre- Cured fabric:
Fabric can be a 100 % cotton fabric or cotton blend. Contrary to all the other WR processes, by this system the fabric does not need any further heat treatment as the curing process has been done already before the shirt is manufactured. The already finished fabric is resistant to wrinkles already. Unfortunately no crisp and sharp creases can be realist for collars, cuffs and front placket edges. As the fabric does not accept any final pressing. Only a shirt finisher with steam and air is required.

## Slide 5
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Post- Cured fabric:
In this case the fabric can be a 100 % cotton fabric or a cotton blend. The fabric will be delivered with the curing chemical inside. The roll of fabric is sealed in a polyester bag . Once the bag is opened the fabric has to be manufactured entirely, as it cannot be stored for a long time. After the shirt is manufactured, it has to be pressed entirely. After it has been put on a hanger it will be cured in a hanging position on a cloth rack inside an oven for 3- 5 min. by about 130°C to 150”C (depends on the chemical used).
Now the shirt is ready for folding and bagging.

## Slide 6
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Dip- Spin system/ The immersion method:
This one belongs to the most popular process for wrinkle free shirts and can be used for 100 % cotton fabrics or cotton blends. After the shirt is manufactured as usually, it will be dipped into a mixture of chemicals, which will be absorbed by the cotton fibres. After the treatment in a tumbler the shirt is still moisturized and has to be pressed entirely. Important is, that during the pressing operation on the various parts Collar-, Cuff- and Body- Presses, the curing process will start already. After pressing the shirt will be put on a hanger and can be cured in a curing oven by about 140°C for about 3 -5 min. One of the key factors for a perfect appearance is the pressing quality, as after the curing operation in an oven, all wrinkles will stay for life. A re-touching by an iron is impossible.

## Slide 7
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
METERED ADDITION PROCESS:
1. Dye and finish the product for a specific fashion look.
2. Spray garment or product with the finishing agent in a rotating chamber. Tumbling continuous untill product is uniformly processed.
3. Hand and performance can be adjusted with fabric softeners and other compounds so that the finished product will appeal to consumers.
4. Press desired features ( creases, pleats, etc.,) into a garment with appeal to consumers.
5. Cure the product in curing oven at 300F for 5 to 15 minutes.
6. Used for fashion apparels and furnishings of 100% cotton.

## Slide 8
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Vapor – Phase:
This curing system can be used in some countries only as very aggressive chemicals are used. Similar to the DIP SPIN system the shirt is manufactured as usually. After the final pressing, a special curing oven is used as instead of liquid chemicals, gas is used to make the shirt resistant to wrinkles. The gas is circulating through the oven and penetrates into the cotton fibre. After a while the gas has to be evacuated from the oven. Before the shirt is folded and bagged, it needs to be washed in order to remove left chemicals inside.

## Slide 9
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
MCQ
https://docs.google.com/forms/d/e/1FAIpQLSeUsQc4-cjTqftxQXSR-aeYZNq1MHRyN-h9W4CAK0YFJnhouQ/viewform?usp=sf_link