## Slide 1
Hindusthan
College of Arts & Science
An Autonomous College- Affiliated to Bharathiar University
Approved by AICTE and Govt of Tamilnadu
Accredited by NAAC- An ISO Certified Institution
Class: III BSc COSTUME DESIGN &FASHION
SUBJECT:TEXTILE FINISHING TECHNOLOGY

## Slide 2
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Dyeing is the application of dyes or pigments on textile materials such as fibers, yarns, and fabrics with the goal of achieving color with desired colorfastness. Dyeing is normally done in a special solution containing dyes and particular chemical material.
UNIT – 4
DYEING:
Introduction and definition in latest dyeing methods: Textiles and garments, latest – Supercritical Fluid Dyeing technology, natural dyes, Bio degradable dyes, Azo free dyes, Fibre reactive dyes, Ultra sonic dyes, Ozone technology.

## Slide 3
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
There are three categories:
Cellulose fiber dye.
Protein fibers dye.
Synthetic fibers dye.
THERE ARE MANY CLASS OF DYE IN THE FOLLOWING:
Reactive dye:
Reactive dye is a common dye in the garments & textile industry. Normally, it is a very highly colored organic substance. Reactive dye are capable of a direct reaction with a fiber substrate. The dyestuff forms a chemical link with the fiber. It is very good fastness properties. Normally, reactive dyes apply in cotton, linen, viscose, wool & Silk.

## Slide 4
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Disperse Dye
Disperse dye is also a very common dye in the garments & textile industry. Disperse dye is originally developed for the dyeing for cellulose acetate & water-insoluble. Normally, it can be used for dyeing nylon, cellulose acetate, polyester & acrylic fiber. Normally, this dyeing temperature is high & more pressure for the dye bath. It is good for fastness properties.

## Slide 5
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Direct Dye
The direct dye is commonly used on cotton fiber or cotton fabric in garments & textile industry. It is also a popular dye in this sector. Generally, this dye mixed in all-purpose dyes with Acid dyes. The wash fastness of this dye is not very good but light fastness is very good. This fastness property can be improved after treatment.
Basic dye
The most common synthetic dye is a basic dye. Initially their color base prevents them from being water-soluble. They can be made so with the base being converted into a salt. basic dyes are reacts with acidic groups or mordants in the fiber. It is very good fastness properties of acrylic fibers & good brightness.

## Slide 6
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
Acid dye
Normally, the acid dye is used for protein fibers & it depends on fabric type. Acid dye applies to wool, silk,& nylon. It looks like a strong caustic soda. But, in reality these dyes are non-caustic acids and sometimes also non-toxics. In some cases mild acids like vinegar are used in the dyeing process. Its fastness properties focus on fabric nature.
Sulphur dye
Sulphur dye is mainly used for cellulose fibers. It can be used for dyeing staple fibers & yarns. It is luster grains & makes a black shade with having a slight reddish or greenish impact. It is used for cotton, viscose & rayon. Its properties have good lightfastness.

## Slide 7
Online Class (Google Meet): Prepared by Deepa.V Date:07.09.2021, Class : III BSc CDF
https://docs.google.com/forms/d/e/1FAIpQLSfTw3GrJTDgxPXhvNTx-sD59SmTFtZHDTsCw4tO2iTgwMxzXQ/viewform?usp=sf_link
MCQ