## Slide 1
SUBJECT : (19CDU17) TEXTILE FINISHING TECHNOLOGY
CLASS : III BSc –CDF

## Slide 2
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
Anti Static Finishing
During spinning, weaving and finishing of yarns and fabric, friction will be created by rubbing .Therefore Hydrophobic fibres tend to develop static charge. As the cellulosic fibres are good conductors, they do not produce static charge whereas the synthetic fibres which are not good conductors, develop static charge.
Due to this, shocks are experienced while working on the stenter, zero-zero machines etc, and the fabrics get entangled and soil attraction takes place which is also a problem. Therefore the synthetic fabrics are given a finish to prevent the static charge generation. This is known as 'Anti static Finish.

## Slide 3
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
Soil or stain release
Soil or stain release is a chemical finish that permits relatively easy removal of soils with ordinary laundering. The finish that allow stains to leave the fabric faster and makes fabric cleanable without significant loss of soil release properties. Soil release is the term used to describe the clean ability of the fabric by the laundering process.
Silicone finishes
Silicone finishes for textiles offer durable soft finish to cotton and its blended fabrics apart from offering aesthetic features. The commonly used silicones in textiles have amino, amido, organo and epoxy functionalities.

## Slide 4
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
silicone based textiles have many advantages. It can reduce shrinkage, scratch free, wrinkle free, add softness to the fabric, has higher water repellency. Silicone coating on fabric maintains the suppleness of the fabric and it does not become hard in cold or decay when exposed to high temperature.
Phase change materials
Phase change materials (PCMs) are substances which absorb or release large amounts of so-called “latent” heat when they go through a change in their physical state, and is more often applied to manufacture the smart textiles.

## Slide 5
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
Fragrance finishing
Fragrance finishing is the process of imparting aroma in any textile substrate. When the fabric gets abraded with our body, the Fragmatic or aromatic atoms are broken out and produce fragrance odor. Finally, the developed product has been subjected to perfume or aromatic finish. Hence, the finish has Called as Fragrance finish.
The finish is wash durable; Perfumes used in aroma finish are safe for children garments. The type of perfume used in this finish ware different and applied as per demand. It is special type of finishing.

## Slide 6
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
A sun-resistant fabric is one that has been treated to withstand UV rays, which account for approximately 10% of the sun's light. UV stands for “ultraviolet,” which is a form of light wave or radiation.
ULTROVIOLET ABSORBENT FINISHES:
A sun-resistant fabric is one that has been treated to withstand UV rays, which account for approximately 10% of the sun's light. UV stands for “ultraviolet,” which is a form of light wave or radiation.
SPF is referred to as the ultraviolet protection factor (UPF). A fabric with an SPF of > 40 is considered to provide excellent protection against UV radiation. UV protective treatment is given to industrial fabrics for awnings, canopies, tents and blinds.

## Slide 7
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
Antislip agents prevent the displacement of threads in woven fabrics. As a result, both slip resistance and seam strength are improved.
Delicate knitted fabrics are prone to snagging. This tendency can be reduced by finishing with PERIPRET auxiliaries. In order to improve luster and smoothness, especially for textiles made of cotton
Anti Pilling Finishing
Pilling is the formation of small knots of fibres on surface of the fabric. This entanglement of fiber spoils the appearance of The fabric.
the main reason for this formation of pills is that the high tenacity fibres like 'PET, Nylon form pills. The problem of pilling is mainly in polyester blends.

## Slide 8
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021

## Slide 9
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
Abrasion resistance
Abrasion resistance is the ability of a fabric to resist surface wear caused by flat rubbing contact with another material. Abrasion resistant fabric withstands surface wear from rubbing, extending the life of a product and protecting the person who wears it.

## Slide 10
Onlineclass(Googlemeet) Prepared by : V.Deepa Class: III.B.Sc CDF 11/08/2021
MCQ
https://docs.google.com/forms/d/e/1FAIpQLSdqR_V8RozEC0xWuahqHxVhJjKb2b9D2jQo9ma2IymrpT-04Q/viewform?usp=sf_link