## Slide 1: FUNDAMENTALS OF TEXTILES
UNIT – 1
INTRODUCTION TO TEXTILE FIBERS

## Slide 2
Classification of textile fibers
Natural fibers
Man-made fibers
Vegetable fiber
Animal fiber
Mineral fiber
Re-generated/
Semi-synthetic fiber
Synthetic fiber
Inorganic fiber
Cotton (seed fib.)
Sisal (leaf fib.)
Jute (bast fib.)
Bamboo (stalk fib.)
Coir (fruit fib.)
Wool (sheep)
Silk (silkworm)
Asbestos
Viscose rayon
Modal
Acetate
Nylon
Polyester
Acrylic
Polypropylene
Metal
Glass

## Slide 3
TEXTILE FIBERS
Textile fibres can be defined as the textile substance that is very small in diameter in relation to their length or in other words fibre is the material which is several hundred times longer than its thickness. Fibre is the basic component of any textile material. There are different types of fibres around us in daily use. Fibres with a short length are called as staple fibres, whereas fibres with long length are called as filaments.
NATURAL FIBERS:
Fibres which are obtained from the natural origin directly or indirectly referred as natural fibres. Fibres obtained from the natural origin can be further sub-classified into three different categories based on their different natural origins;
      Vegetable fiber
      Animal fiber &
      Mineral fiber

## Slide 4
VEGETABLE FIBER
These fibres are basically cellulosic fibres. Besides their use as textiles, these fibres are also used in the manufacturing of papers. Vegetable fibres are basically obtained from various parts(Organs) of the plants such as seeds, bast, leaf, fruit, stalk, etc.
Seed fibres;
These are obtained from seeds such as cotton, kapok, etc. the cotton fibres are widely used for the apparel purpose, medical uses, and other textile applications.
Leaf fibres;
These are obtained from leaves of plants such as sisal, agave, etc. Leaf fibres are used for marine ropes and cement reinforcement.
Fruit fibres;
These are obtained from the fruit of the plant such as coir fibre (coconut fruit). These fibres are mainly used for manufacturing doormats, carpets, etc.
Bast fibres;
Bast fib. are obtained from the bast surrounding to the stem of the plant. Such as jute, hemp, flax, ramie, etc. These fibres have more strength, durability and do not get affected by moisture so that they are used for manufacturing durable yarns, fabrics, packaging material and paper.
Stalk fibres;
Extracted from stalks of the plant – such as straws of rice, wheat, and other crops. Bamboo and grass fibre is also included.

## Slide 5
2. ANIMAL FIBER
The fibres are obtained from animals are called as animal fibres. The fires are mainly made up of protein molecules. The basic element of a protein molecule is carbon, nitrogen, hydrogen, oxygen.
Wool (Hair fibres obtained from the animals) & silk fibres are common examples of animal fibres.
Wool;
The fibres obtained from the sheep are referred as wool fibres, in the way the hair of the horse, camel, goat are also obtained as fibre. 90% of hair fibres are wool fibres used various applications.
Silk;
It is very delicate filament. It is obtained from silkworms. Silk formation takes place by the secretion of proteinous molecules in liquid form through the glands of the silkworm, It is located on the head of the worm. This liquid proteinous material gets converted into the solid filament. During this secretion process, the worm forms cocoons from which silk is extracted. The sericulture of the silkworm is called as the rearing of the silkworm.
3. MINERAL FIBRES
These are the inorganic materials shaped into fibres. Asbestos is the example of mineral fibre. These fibres are fireproof, resistance to acid so that these fibres mainly found in the industrial application.

## Slide 6
MAN-MADE FIBERS
As the name itself indicates these textile fibres are made by man to meet the particular requirements. The chemical composition, structure, and properties are significantly modified during the manufacturing process. Depending on the raw material chosen for making these textile fibres – fibres can be further subclassified into 3 categories ;
Regenerated Man-Made
Synthetic Fibres
In-Organic Fibres
1. REGENERATED SYNTHETIC;
Regenerated synthetic textile fibres are also called as semi-synthetic fibres. These fibres are made up of naturally long chain polymer structure, which is modified and partially degraded by a chemical process to enable the polymerization reaction to form the fibres. Most of the semi-synthetic fibres are called cellulose regenerated fibres. Examples: Viscose rayon, modal, cupra (Rayon), bamboo viscose, tencell.

## Slide 7
2. SYNTHETIC FIBER;
Synthetic fibres are manufactured from the petrochemicals.
Examples – Polyester, nylon, acrylic, etc. These fibres are formed by the polymerization of monomers.
Once the polymer is formed, it can be formed into a filament by converting that polymer into fluid form and then extruding the molten or dissolved polymer through narrow holes to give filaments. To form the fibre from molten polymer it gets passed through the spinneret. These fibres are generally very strong, fine and durable with very low moisture absorbency property so that these fibres are also called as hydrophobic fibres.
3. INORGANIC FIBER
These textile fibres are also called as metallic fibres. Metallic fibres are drawn from the ductile metals such as copper, gold, silver and can be extruded or deposited from more brittles such as nickel, Aluminum and iron. From stainless steel also fibres can be formed. These fibres are not that much widely used but these fibres have their special applications in technical textile.

## Slide 8
PRIMARY & SECONDARY CHARACTERISTICS OF TEXTILE FIBERS
PRIMARY CHARECTERISTICS OF TEXTILE FIBERS
Staple length ;
Staple refers to textile fiber of discrete length. The opposite is a filament fiber, which comes in continuous lengths. Staple length is an important criterion for spinning fibre, as shorter fibres are more difficult to spin than longer ones, so staple length varies from short to longer length fibres, short fibers also resulting in more hairy yarns.
Tensile strength ;
Tensile strength can be defined as the maximum stress that a material can bear before breaking when it is allowed to be stretched or pulled.
Fineness ;
Fiber fineness is one the most important fiber characteristics. The Fiber fineness determines how many fibers are present in the cross-section of a yarn of given thickness. Fiber fineness plays an important role in determining the quality of resultant yarn and hence that of the resultant fabrics.

## Slide 9
Spinnability ;
The quality of being suitable for spinning or the capability of being spun.
Uniformity ;
Uniformity means the evenness of the individual fibres in its length and diameter. A fibre possessing this property can produce reasonably even yarns. This is also important in connection with the strength of the resulting yarn. Uniform textile fibres should possess uniformity in their thickness and length.
SECONDARY CHARECTERISTICS OF TEXTILE FIBERS
Crimp ;
Crimp in a textile strand is defined as the undulations or succession of waves or curls in the strand, induced either naturally during fiber growth, mechanically, or chemically.

## Slide 10
Elasticity ;
Elasticity plays dominant role in prognosis the behaviour of fabrics during wearing as well as in estimating their durability.
Absorbency ;
Absorbency is used to describe the ability of a fabric to take in moisture – a very important property, which affects many other characteristics such as skin comfort, static build–up, shrinkage, water repellency and wrinkle recovery.
Resilience ;
The ability to return or 'spring back' to the original form or position after being bent, compressed or stressed and is used as a measure of the elastic properties of a material.
Lustre ;
lustre or luster is a physical property that makes them appear bright, glossy, and shiny. The amount of light reflected from the surface of a fiber is referred to as its luster.

## Slide 11
Rigidity ;
The ability to resist the bending of fabric is called fabric stiffness. It is a measure of the resistance of a fabric to bending by external forces.
Abrasion ;
Abrasion is a kind of wear in which rubbing away of component fibers and yarns of the fabric takes place. During abrasion, a series of repeated applications of stress takes place.

## Slide 12
PROPERTIES & USES OF NATURAL FIBER
PROPERTIES OF COTTON FIBER :
Can be damaged by mildew
Can be damaged by prolonged exposure to sunlight
Comfortable to wear
Cotton fabric is very absorbent fabric because there is a lot of space between the cotton fibers.
Cotton have better breathability
Can withstand heat, detergents, and bleach
Resists static electricity build-up
Wrinkles easily
USES OF COTTON FIBER :
Cotton is used to make a variety of woven fabrics, including canvas, denim, damask, flannel, and more.
Since cotton is extremely soft and absorbent, it is an ideal fabric for bedroom linens and towels needed to sop up moisture.
Cotton is also used throughout the home for upholstery, curtains, rugs, pillows.

## Slide 13
PROPERTIES OF LINEN FIBER :
Linen can absorb up to 20% of its weight in moisture.
It is the second strongest fabric after the silk. Linen is about 30% stronger than cotton, making linen fabrics durable for several decades
It draws heat away from the body, keeping you cooler in the warmer months and gives warmth during the cold months of the year.
Being a natural fiber it is really cosy and comfy to wear.
Great abrasion resistant. As linen is good in strength, it also has good abrasion resistance.
Because of the natural flax, there are no allergic reactions using linen and hence it is helpful in treating a number of allergic disorders.
USES OF LINEN FIBER :
Linen is used to make household items such as tablecloths, upholstery, soft furnishings and curtains. It is also used for making many types of garment and for making a strong sewing thread. Linen is often embroidered, especially on women’s clothes and household items. The use of linen has changed. In the 1970s about 5% of linen was used for fashion while the rest was used for household items. However, about 70% of linen production is now used for fashion.

## Slide 14
PROPERTIES OF SILK FIBER :
Silk is a lightweight, breathable fabric, which means it reduces the risk of overheating
Silk is fairly absorbent. Water weakens the fibres, though, so treat your silk carefully when you’re washing it.
Silk fibres are smooth and straight, unlike wool, for example, which has a scaliness you’ll see if you put it under a microscope. This difference makes silk smoother to the touch and shinier to the eye, with an altogether luxurious feel.
Silk’s good at maintaining your body temperature.
USES OF SILK FIBER :
Besides silk being used as garments it is also used in other industries and for military purposes. It is used in the manufacture of fishing fibres, parachutes, cartridge bags, insulation coils for telephones and wireless receivers, tyres of racing cars, filter clothes for flour mills, and in medical dressings and suture materials. Insulation coils for telephones and wireless receivers, tyres of racing cars, filter clothes for flour mills, and in medical dressings and suture materials.

## Slide 15
PROPERTIES OF WOOL FIBER :
As wool fiber retains a certain amount of air moisture, it is good fire resistant.
This prevents mildew, and other undesirable “stinks”.
Wool does not absorbs water.
Low heat has no effect but strong heat weakens the fibre and destroys the colour of the fibre.
It is stronger than silk. When wet wool loses about 25% of its strength. The longer the fibre the greater will be the strength of the yarn.
Wool is highly elastic.
Wool is resistant to shrinkage.
USES OF WOOL FIBER:
Being easy to clean and lasts long, preferred for clothing.
The most important use of wool is for apparel coats, jackets, suits, dresses, skirts, slacks made from woven fabrics of varying weights and knitted fabrics.
Acts as insulator, hence used for bedding and blankets.
Used to line boxes, shelf linings and surfaces required to be softer.
In the home furnishing area, the major use of wool is in carpets and rugs where wool is used more, cover to the carpets and warm in the rugs.

## Slide 16
PROPERTIES OF BANANA FIBER :
It is a strong fiber and has lower strain at break.
Its appearance is quite shiny, which depends on the extraction and spinning processes.
It has low density and strong moisture absorption quality.
Its absorbance and release of moisture are quite fast.
The appearance of banana pseudo-stem fiber is quite like ramie and bamboo fiber, but its spin ability and fineness are much better than that of ramie and bamboo.
USES OF BANANA FIBER :
Banana pseudo-stem fiber is utilized to produce cushion cover, bag, table cloth, curtain, and others
This fiber is also used to produce fishing nets, other types of cordage, mats, packaging, sheets, etc.
Additionally, there are some potential uses of banana fibers, for the production of mushroom, arts/handicrafts, string thread, paper cardboard, tea bag and high-quality textiles/fabric materials, currency note paper, and many other products.

## Slide 17
PROPERTIES OF JUTE FIBER :
100% bio-degradable recyclable and thus environment friendly
Natural fibre with golden & silky shine
The second most important and widely cultivated vegetable fibre after cotton
High tensile strength with low extensibility this helps to make best quality industrial yarn and fabric for packaging
Jute fibers are always known as strong, coarse, environment friendly, and organic.
It has high tensile strength, low extensibility, and ensures better breathability of fabrics. Therefore, jute is very suitable in agricultural commodity bulk packaging.
USES OF JUTE FIBER:
Luxurious range of Jute home decor products are available to suit different life styles. Cushion covers, table mats, table covers add class to the lifestyle. Exquisite Jute floor coverings add ethnicity to home interiors. Be it light, soft and practical portfolio bags for executives, Jute + cotton blend bedspreads, easy to clean decorative wall hangings, soft non-scratching mats/baskets or sturdy and comfortable hammocks they all come in jute - so celebrate this autumn season in an eco-friendly- class of its own way.

## Slide 18
PROPERTIES OF PINEAPPLE FIBER :
Poor sunlight resistance, scorches at high temperature.
Sweat absorbent and breathable fiber.
Hard and not wrinkling properties.
Good antibacterial and deodorization performances.
Shiny as silk
Yarn strength increase by about 50% when wet.
Difficulties in dye penetration due to high coarseness.
USES OF PINEAPPLE FIBER:
Pineapple fiber is sometimes combined with silk or polyester to create a textile fabric, which is lightweight, has an elegant appearance similar to linen and easy to care.
The pineapple threads have also been used for long in India and China for lines and threads and as an adulterant in silk.
Pineapple leaf fiber is also used for table linens, bags, mats and other clothing items, where lightweight and stiff fabric is needed. The characteristics of the fabric made from pineapple fiber make it ideal for high grade suits, shirts, divided skirt, decorative fabrics and so on.

## Slide 19
PROPERTIES OF HEMP FIBER :
The penetration of dye is easy in hemp
It obstructs ultra violet (UV)
Has natural anti-bacterial properties.
Elastic recovery is very poor. It is less than linen fiber.
Mildews and bacteria will flourish on hemp under hot and humid conditions. They can be protected by impregnation with certain types of chemicals. Copper Naphthenate is one of the chemicals.
It has enough ability to prevent the bad effect of sunlight.
USES OF HEMP FIBER:
It is ideal for making ropes, twine, cables, carpets, sail cloth, canvas, ship cordage etc.
Hemp is used for wide varieties of purposes, specially the manufacture of cordage of varying tensile strength, clothing and nutritional products.
Hemp is used in tapestry, hats, shawls, rugs, posters, and towels.
Dyed hemp yarn from Hungary is suitable for rug weaving, placemats, crochet, and other craft items.

## Slide 20
________End of the slide________